800kVA Enclosed Generator Set

Rated at N.T.P. Conditions

Macfarlane Generators has been connected with this FG Wilson model DDC800E enclosed generator since delivering it in January 1998. It shows 6913 hours and being in excellent condition, is ideal for Prime or Standby power generation.

Engine:	DETROIT 16V92TA Turbocharged, liquid cooled, 2 stroke, electric start diesel

HP:				 1025 approximately

RPM:				 1500

Cylinders:			 16V

Run Hours Shown:		 06913

Alternator:	STAMFORD HC6I34G

kVA:				 800 Standby rated (720kVA Prime rated)

kW:		 640 Standby rated (576kW Prime rated)

Power Factor:		 0.8

Other:				 240/415V at 50Hz, brushless

Including:	Acoustic canopy with inlet attenuators rated approximately 75dB(A) @ 7mtrs

Substantial base including 4 x lift points

1 x single 36W ceiling mounted fluorescent batten interior light

Two only access doors to each side

Dimensions LxWxH: 5725x2200x3500mm including the roof mounter muffler

Internal single wall fuel tank approximately 1300 litres, approximately 8 hours running @ 75% load

Battery pack heavy duty 24 Volt with automatic charger

Deep Sea Electronics DSE509 control panel with automatic remote/manual starting

Engine protection for low oil pressure, high coolant temperature, low coolant

Analogue battery charging volt meter

Analogue oil pressure gauge

Generator mounted 1250 Amp 3 pole Terasaki S1250NE adjustable circuit breaker

Build date: 1995

Cleaning, detailing and a load test with report

Operating manuals

Reference:	U537